## Slide 1: CGRA Virtualization
Kalhan Koul

## Slide 2: Outline
SoC Review
    Quick Overview
Spatial Virtualization
Temporal Virtualization

## Slide 3: Amber architecture
Processor Subsystem
- ARM Cortex-M3
- Runs software to control CGRA
CGRA Subsystem
- Global Buffer
- Global Controller
- Tile Array (PE, MEM)
- Hardware acceleration occurs
DMA Subsystem
- Two DMAs
Peripheral Subsystem
TLX Subsystem

## Slide 4: SoC architecture
Processor Subsystem
- ARM Cortex-M3
- Runs software to control CGRA
CGRA Subsystem
- Global Buffer
- Global Controller
- Tile Array (PE, MEM)
- Hardware acceleration occurs
DMA Subsystem
- Two DMAs
Peripheral Subsystem
TLX Subsystem

## Slide 5: SoC architecture
Processor Subsystem
- ARM Cortex-M3
- Runs software to control CGRA
CGRA Subsystem
- Global Buffer
- Global Controller
- Tile Array (PE, MEM)
- Hardware acceleration occurs
DMA Subsystem
- Two DMAs
Peripheral Subsystem
TLX Subsystem

## Slide 6: CGRA Architecture

## Slide 7: CGRA architecture
Global Buffer
- Communicate with the SoC system with AXI4 and AXI4-Lite interface
- 1D array of GLB Tiles with two banks
- I/O controller streams data into/out of CGRA
- It streams the bitstream into CGRA
CGRA
- Island-style mesh network with PE nodes and MEM nodes
- Divided into groups of columns

## Slide 8: The basic control flow to run an application on CGRA
1. DMA streams bitstream to GLB
2. DMA streams to input data GLB
3. M3 configures I/O controller
4. M3 sends config_start signal I/O controller
5. M3 sends kernel_start signal to I/O controller
6. CGRA array runs a kernel
7. I/O controller sends an interrupt signal to M3
8. DMA streams output data out of GLB
data
control
comp.
data

## Slide 9: The basic control flow to run an application on CGRA
1. DMA streams input data to GLB
2. DMA streams bitstream to GLB
3. M3 configures I/O controller
4. M3 sends config_start signal I/O controller
5. M3 sends kernel_start signal to I/O controller
6. CGRA array runs a kernel
7. I/O controller sends an interrupt signal to M3
8. DMA streams output data out of GLB
data
control
comp.
data

## Slide 10: The basic control flow to run an application on CGRA
1. DMA streams input data to GLB
2. DMA streams bitstream to GLB
3. M3 configures I/O controller
4. M3 sends config_start signal I/O controller
5. M3 sends kernel_start signal to I/O controller
6. CGRA array runs a kernel
7. I/O controller sends an interrupt signal to M3
8. DMA streams output data out of GLB
data
control
comp.
data

## Slide 11: The basic control flow to run an application on CGRA
1. DMA streams input data to GLB
2. DMA streams bitstream to GLB
3. M3 configures I/O controller
4. M3 sends config_start signal I/O controller
5. M3 sends kernel_start signal to I/O controller
6. CGRA array runs a kernel
7. I/O controller sends an interrupt signal to M3
8. DMA streams output data out of GLB
data
control
comp.
data

## Slide 12: The basic control flow to run an application on CGRA
1. DMA streams input data to GLB
2. DMA streams bitstream to GLB
3. M3 configures I/O controller
4. M3 sends config_start signal I/O controller
5. M3 sends kernel_start signal to I/O controller
6. CGRA array runs a kernel
7. I/O controller sends an interrupt signal to M3
8. DMA streams output data out of GLB
data
control
comp.
data

## Slide 13: Flexible buffer allocation
input
output
Case1 (Flexible GLB Allocation)
- One kernel
- Input buffer (4 banks)
- Output buffer (4 banks)

## Slide 14: Multiple kernels in parallel
Case2 (Multiple Kernels in Parallel)
- Three kernels
- Different kernels run in different regions of the CGRA
- Independent control of each kernel (start, interrupt)
kernel1
kernel2
kernel3

## Slide 15: End-to-End Applications

## Slide 16: Conducting an Application with the M3 Core
Initialize System
    Enable UART, DMA engines, etc.
    Select Clocks, Interrupts, etc.
Bring in Configuration and Input Data
    Use DMA engines to move data (bitstream, images, etc.)
    From DRAM/SRAMs to Global Buffer
Configure Global Buffer and Run Kernel
    Use Parallel Configuration to send the bitstream to the CGRA
    Stream in input data and stream out output data
Repeat Step 2 and 3 per Application
Finish Application
    DMA Output Data to DRAM
    Send done information to Host Processor

## Slide 17: Conducting an Application with the M3 Core
Initialize System
    Enable UART, DMA engines, etc.
    Select Clocks, Interrupts, etc.
Bring in Configuration and Input Data
    Use DMA engines to move data (bitstream, images, etc.)
    From DRAM/SRAMs to Global Buffer
Configure Global Buffer and Run Kernel
    Use Parallel Configuration to send the bitstream to the CGRA
    Stream in input data and stream out output data
Repeat Step 2 and 3 per Application
Finish Application
    DMA Output Data to DRAM
    Send done information to Host Processor
​Off Chip: Bitstream, Input Data

## Slide 18: Conducting an Application with the M3 Core
Initialize System
    Enable UART, DMA engines, etc.
    Select Clocks, Interrupts, etc.
Bring in Configuration and Input Data
    Use DMA engines to move data (bitstream, images, etc.)
    From DRAM/SRAMs to Global Buffer
Configure Global Buffer and Run Kernel
    Use Parallel Configuration to send the bitstream to the CGRA
    Stream in input data and stream out output data
Repeat Step 2 and 3 per Application
Finish Application
    DMA Output Data to DRAM
    Send done information to Host Processor
​Bitstream, Input Data

## Slide 19: Conducting an Application with the M3 Core
Initialize System
    Enable UART, DMA engines, etc.
    Select Clocks, Interrupts, etc.
Bring in Configuration and Input Data
    Use DMA engines to move data (bitstream, images, etc.)
    From DRAM/SRAMs to Global Buffer
Configure Global Buffer and Run Kernel
    Use Parallel Configuration to send the bitstream to the CGRA
    Stream in input data and stream out output data
Repeat Step 2 and 3 per Application
Finish Application
    DMA Output Data to DRAM
    Send done information to Host Processor
Configure CGRA to Layer 1
Stream Input/Output
Configure CGRA to Layer 2
Stream Input/Output
…
Configure CGRA to FC Layer
Stream Input/Output

## Slide 20: Conducting an Application with the M3 Core
Initialize System
    Enable UART, DMA engines, etc.
    Select Clocks, Interrupts, etc.
Bring in Configuration and Input Data
    Use DMA engines to move data (bitstream, images, etc.)
    From DRAM/SRAMs to Global Buffer
Configure Global Buffer and Run Kernel
    Use Parallel Configuration to send the bitstream to the CGRA
    Stream in input data and stream out output data
Repeat Step 2 and 3 per Application
Finish Application
    DMA Output Data to DRAM
    Send done information to Host Processor
​Output Data

## Slide 21: Motivation for Virtualization
Two users access server for application acceleration
  Most domain specific accelerators will schedule one after the other with high PE utilization
  CGRA gives us opportunity to do both in parallel, to achieve high PE utilization
Two sensors need immediate processing
  CGRA gives us opportunity to do both in parallel on the same accelerator, simplifying SoC architecture and scheduling management

## Slide 22: Partitioning Algorithm

## Slide 23: Temporal Scheduling
The M3 and Global Buffer pairing allow us to efficiently schedule applications
For example: a batch of images with the same kernel
Cycles to put an image in GB ≈ cycles to stream an image to the fabric
Can Send Output 1 and Load Image 3 at same time with 2 DMAs
Load Image 1
Stream Image 1
Send Output 1
Load Image 2
Stream Image 2
Send Output 2
Load Image 3
Stream Image 3
Send Output 3

## Slide 24: Place PE Utilization stream slide from DARPA

## Slide 25: Spatial Scheduling
With the M3 we can place more than one kernel onto the fabric at once
For example: a conv3x3 and harris configured to two halves of the CGRA
With 2 DMAs we can run both applications independently
Conv 3x3
Harris
Load Image 1
Stream Image 1
Send Output 1
Stream Bitstream 1
Load Image 2
Stream Image 2
Send Output 2
Stream Bitstream 2

## Slide 26: Place Demosaic + Conv3x3 Slides from DARPA

## Slide 27: Dynamic Scheduling Slide

## Slide 28: Autoscheduling Slide

## Slide 29: Virtualization Summary
Variety of scheduling decisions due to the complexity of our system (DMA, GLB, CGRA, etc.)
    Tiling at DRAM level
    Tiling at Global Buffer level
    Overlapping of Data Movement, Kernels, Configuration etc.
Currently most of our applications are scheduled statically, but ...
Autoscheduling is the next step