## Slide 1: Physical Design Flow for Garnet SoC
Alex Carsello

## Slide 2: What we’re taping out
32x16 array of CGRA tiles (possibly larger)
4 MB of SRAMs (256 individual macros)
Analog block
Processor subsystem
  Cortex M3
  A few SRAMs
  Not large (1-2% of total chip area)
Global Buffer SRAM Array
SoC processor subsystem
Analog block

## Slide 3: Current Physical Flow
Hierarchical physical design flow
Full P&R flow for each tile type (PE and Memory)
Then essentially do everything else at the top-level
  Manually place all SRAM macro arrays using flexible/parameterized procedures
  Manually abut the tiles
    No interconnect routing required because adjacent tiles are connected by abutment
  Create soft regions for Global buffer, CGRA, and processor subsystem logic
  Tool places and routes all cells for global buffer control, processor subsystem,

## Slide 4: Complexities
Creating abutted CGRA tiles
  Need to ensure that connecting pins on adjacent tiles align exactly
All kinds of grids
  Routing grids for tile pin layers (M3-M6)
  FinFET grid
  Standard cell row grid
  Need to place macros such that all pins end up on the preferred routing tracks for their layers
Ensure power stripes inside tiles line up with top-level power stripes, so that power grid at top-level is uniform across the chip

## Slide 5
CGRA
Global Buffer SRAMs
ARM processor subsystem
Preliminary floorplan with pads, CGRA tiles, and memory macros placed
Analog block will be placed in top center
Pad placement still needs to be optimized with package in mind to make RDL routing easier/possible
We may be able to make the tile array and global buffer SRAM array larger
Changes I’ve already made to this (sorry I couldn’t update the screenshot on the plane):
  Moved ARM processor subsystem to bottom right corner Global buffer SRAMs straddle alignment cells
Alignment cells

## Slide 6: Improvements made to the flow
QoR improvements:
  Targeting much higher clk frequency and area efficiency
Trying to make it such that design changes only need to be made in one place using the following techniques:
  Introspecting the design rather than using hard-coded values for different physical design parameters
  Everything technology-dependent is a parameter (and all of these parameters are in one place in the physical design flow scripts)
  (Almost) everything design-dependent is calculated by introspecting the design and taking into account a small set of parameters/constraints: tile sizes, power stripe pitches, tile grid dimensions

## Slide 7: Problems that still need to be addressed
DRCs
  Around 20K DRCs at top-level right now (not as scary as it sounds! But still needs to be addressed. Many of them appear to have the same root cause).
Timing Closure
  Individual tiles are meeting timing at just above 400 MHz, but top level P&R is running with extremely lax constraints to reduce P&R runtime as I debug/finish the PD flow
Global signal buffer insertion
  Need to calculate proper buffer sizes for all global signals and insert at tile-level. Can’t do this at the top because of the abutted tile floorplan.

## Slide 8: Tapeout Checklist
https://github.com/StanfordAHA/garnet/blob/master/docs/tapeout_checklist.md

## Slide 9: Physical Design Checklist
Timing (source: Primetime, Innovus)
  Primetime hold margin across all scenarios >= xx ns
  Max clock frequency (TC 0.8 V) > xx MHz, (TC 1.2 V) > xx MHz
  JTAG clock always > xx MHz
  Report all static timing analysis overrides (false paths, async boundaries, multicycle paths), make sure they are okay
  Static timing overrides in gate level simulation verified
  Primetime infers clock gating checks
  Clock tree report - reasonable tree depth, insertion delay, skew

## Slide 10: Physical Design Checklist
Physical verification (source: Calibre)
  DRC (primary, antenna, wirebond) - no errors
  ERC - no errors
  LVS - correct
  All of the above pass after dummy fill

## Slide 11: Physical Design Checklist
Power domain related checks (source: Innovus)
  PG nets verified
  Clock tree multi-voltage safety
  check_mv_design (equivalent Innovus command) clean
  Decoupling
  Worst power + group IR drop in Primerail report (static) < xx mV
Other sanity checks
  Bond pad labels match pinout
  All memory stubs replaced by SRAM macros

## Slide 12: Functional Verification Checklist
RTL functional verification (source: pytest log)
  CGRA + GB unit test suite - RTL vs functional model passes
  CGRA + GB integration tests using apps (with SoC stub)
  SoC unit test suite
  SoC integration tests (with CGRA + GB stub)
  CGRA + GB + SoC integration tests (with FPGA stub)
Gate level functional verification
  All of the above pass at gate level with no timing violations
Power domain aware RTL/gate level simulation/formal checking
Formal verification
  RTL vs gates
  Configured CGRA vs CoreIR DAG?
Have to make sure we have enough unit and integration test coverage
-- use testing dashboard