## Slide 1: Next-Gen CGRA Architecture

## Slide 2: System Architecture (1/2)
Clock domain based CGRA
    Allow different part of the chips to operate at different frequencies
Power domain based CGRA
    Multiple power domains on the chip – Low-voltage, Always-on, Shut-down
DVFS (Dynamic voltage frequency scaling) support
    Variable operating voltage & frequency. DVFS can be used for non-timing critical applications
Power Domain based CGRA

## Slide 3: System Architecture (2/2)
  Fast reconfiguration/Run-time reconfigurability
    Configuration currently takes ~100 JTAG clock cycles per configuration register
    Ability to swap out applications quickly
    E.g. mapping different convolution layers in CNN
  CGRA Hardware Virtualization
    Resource re-use when application size is bigger than available hardware resources
    Multi-rate support for different applications
    State machine based design
Resource sharing in CGRA
Representative fast-reconfiguration architecture

## Slide 4: PE Architecture
Analyze the target applications to find frequently occurring common patterns/compute kernels
Improve compute density for PEs
    Current version uses 2 input-PE
    3-input based PE design
      Absolute difference addition, FMA
Support new operations – division, modulo, saturation etc.
Super-PE architecture
    Multi-precision handling
    Virtualization
  Homogeneous vs Heterogeneous PE tiles
    All PEs do not need to support all the functionalities – Improve compute density E.g. LUTs, register files
PE Clustering

## Slide 5: Memory Architecture
Dual ported memory
    Flexible and simpler design compared to single-ported SRAM and additional logic
    Enable irregular access patterns
  Double buffering
    Supply operands out of one buffer while performing LD/ST operations on the other
    Allow hardware to overlap computation and memory loads
  Memory hierarchies
    Optimize data locality
  DMA Engine
    Mem-tile to Mem-tile copying or moving of data within memory
Architecture template with double buffer
& memory hierarchy

## Slide 6: CGRA Connectivity/Routing
Explore dataflows/customized connectivity patterns for a class of applications
  Interconnect architecture exploration
    Trade-offs between flexibility, fanouts and different topologies
Routing Profile Extraction
    List of key switchbox parameters needed for P&R to better evaluate metrics like IO utilization, wirelength length stats, routing density etc.