## Slide 1: CGRA Architecture
PTILE
MTILE
PTILE
PTILE
MTILE
PTILE
16 bit bus
1 bit bus
Switch box
16 bit CB
1 bit CB
J
T
A
G
Global Control
Host
CGRA

## Slide 2: CGRA Specifications
TSMC 16nm FFC PODE 10 ML
5mm x 5mm ; Flip Chip ; PIO
16x16 CGRA grid (192 PE : 64 Mem)
64 programmable IOs
Tile addressable JTAG configuration
2KB per tile, 128KB total on-chip memory
Single, always-on, power domain
Uni-clock architecture
Four 1-bit programmable global signals
CGRA Final Layout

## Slide 3: Automating Physical Design
Eight weeks from RTL to Tapeout
Significant effort spent in getting a DRC clean PAD ring and core area
PnR challenges when routing global signals across a die with non-boundary tile macros and long narrow channels
Regular grid structure can be exploited to simplify PnR
CGRA Verilog generator can also generate collateral for directing the PnR tool (UPF/CTS/etc.)
Chart: Tapeout Effort
| Technology Bringup | Flow Bringup | Design Bringup | DRC/LVS/Finishing Iterations
 | 25 | 10 | 25 | 40

## Slide 5
Innovus - Calibre Mismatch
There were many issues in recent Tape-out(16nm FinFET) when running Full-Chip DRC
All these errors couldn’t be detected in Innovus
Examples
1) FIN / OD off-grid error ( > # 1M)
2) Pin off-grid error ( ~ #100)

## Slide 6
Innovus - Calibre Mismatch
3) Metal spacing errors (~ #200)

## Slide 7
Innovus - Calibre Mismatch
4) Bumps are not connected to PADs (~ #150)
5) Power shortage
bump
pad
no via8
6) Cell misplacements
OD
CPO
filler
filler
filler
filler
filler
filler
decap
boundary

## Slide 8
Innovus - Calibre Mismatch
7) Voltage dependent metal spacing / ESD ( > #300M)
 Absence of back-to-back diode between two grounds causes ESD errors and voltage dependent metal spacing errors
Innovus cannot detect all DRC errors
More than 3 weeks are taken to fix these errors by manual layout revision