## Slide 1
Multi-rate convolution is one usecase for space-time trade-off
    E.g. 3x3 convolution – Full rate with 9 MACs, 1/3rd rate with 3 MACs or 1/9th rate with 1 MAC
Hardware support needed - Register file to store constants, shift register to store data, PE accumulation and counter mode and PE cluster
Minimum area overhead – ~1 % area increase per register relative to PE. PE area relative to tile is only 30%
Application 1: Enable mapping and improve performance of state based kernels like Harris (TODO: Get resource utilization stats from Keyi with/without the PE virtualization hardware (~100x reduction))
Application 2: Improve inference-per-sec (IPS) for classification task using CNNs with multi-rate support
    Alexnet 1st layer: 363 MACs (11x11x3) needed for full-rate CONV
    Assuming 100 PEs on chip – Needs 3 reconfigurations
    Total latency (default) - 26663 CC (363 CC (for computation) + 100*100*2 CC + 63*100 CC (reconfiguration))
    1/4th rate convolution with virtual partitioning – 1452 CC (363*4)
Fast reconfiguration techniques can help improve the reconfiguration latency through JTAG but still be slow compared to virtual partitioning
Space-Time Trade-offs for CGRA using Virtual Partitioning
HW SUPPORT – MULTI-RATE CONVOLUTION
CGRAs assume long computational intervals due to overhead of reconfiguring the hardware substrate
Goal: Maximize the time till the substrate needs to be reconfigured by allowing resource reuse using temporal scheduling of tasks
Re-configuration currently takes ~100 JTAG clock cycles per configuration register
Allow trade-offs between execution time and the hardware resources (space-time trade-offs)
    Useful when lower output rate is needed
    Improve rate-matching across parallel applications to allow simultaneous execution of multiple independent kernels
    Allow footprint reduction for non-timing critical operations by power gating the resources not needed
vs
MOTIVATION