## Slide 1: What Is Interesting To Me Right Now …
6/23/2018
Mark Horowitz

## Slide 2: Applications to Hardware

## Slide 3: If You Are Building an Accelerator
The application better be parallel
The application better have locality
Performance/energy must be a critical issue

## Slide 4: Remember It Must Be Cheap To Design
Application designer accessible
Little silicon expertise

## Slide 5: Halide Example: Unsharp Masking
Func clamp, gray, blurx, blury, sharpen, ratio, unsharp;
Var x, y, c, xi, yi;
// The algorithm
clamp = BoundaryConditions::repeat_edge(in);
gray(x, y) = 0.3*clamp(0, x, y)+0.6*clamp(1, x, y)+0.1*clamp(2, x, y);
blury(x, y) = (gray(x, y-1) + gray(x, y) + gray(x, y+1)) / 3;
blurx(x, y) = (blury(x-1, y) + blury(x, y) + blury(x+1, y)) / 3;
sharpen(x, y) = 2 * gray(x, y) - blurx(x, y);
ratio(x, y) = sharpen(x, y) / gray(x, y);
unsharp(c, x, y) = ratio(x, y) * input(c, x, y);
// The schedule
unsharp.tile(x, y, xi, yi, 256, 256)
.accelerate({clamp}, xi, x)
.parallel(y).parallel(x);
in.fifo_depth(unsharp, 512);
gray.fifo_depth(ratio, 8);
// other schedules...

## Slide 6: Architecture Template: Stencil Functions and Line Buffers
Stencil functions consume sliding windows of data
  Huge locality
To capture this locality need to buffer a few lines
  Line buffer is the hardware buffer block.

## Slide 7: Dataflow IR Transformation
Pu, Jing, et al. "Programming heterogeneous systems from an image processing DSL." ACM Transactions on Architecture and Code Optimization (TACO) 14.3 (2017): 26.

## Slide 8: DNN Accelerators
[1] https://cloudplatform.googleblog.com/2016/05/Google-supercharges-machine-learning-tasks-with-custom-chip.html
[2] https://www.electronicsweekly.com/news/ifa-2017-huawei-reveals-low-power-kirin-970-mobile-ai-chipset-2017-09/
[3] http://eyeriss.mit.edu/
Google TPU
Huawei Kirin NPU
Eyeriss
C. Zheng, et al (FPGA)
Can represent them as different schedules to a Halide program.
Notes: Industry
TPU, optimize for latency, big matrix multiply unit
Diannao, NLR
Eyeriss, optimize all kinds of data reuse, …
Zhang, FPGA, flexibility

## Slide 9: Architecture Template for DNNs

## Slide 10: Dataflow Impact
Most dataflows achieve close-to-optimal energy efficiency

## Slide 11: Energy Breakdown Comparison
Use a smaller register file size can greatly improve overall energy efficiency, by reducing register file energy

## Slide 12: What Are Other Applications Classes?

## Slide 13: Connect Hardware to User Process

## Slide 14: AHA CGRA Architecture
TILE
TILE
TILE
TILE
TILE
TILE
16 bit bus
1 bit bus
Switch box
16 bit CB
1 bit CB
Design Space Exploration:
Tile Design
Programmable Routing
Tile Clustering
Memory Topology

## Slide 15: Area Breakdown for Simple 2:1 PE

## Slide 16: Clustering