## Slide 1: Garnet: The Next Generation CGRA Architecture
Priyanka Raina
May 10, 2019

## Slide 2: Challenges with Jade CGRA
1. PE supports only simple integer operations
  Porting applications that use floating point requires application expertise and manual effort

## Slide 3: Challenges with Jade CGRA
Memory supports only line buffered pipelines
  Most new applications even for imaging and vision use neural networks
  Need a memory hierarchy with double buffers for energy-efficiency
3 3 convolution
Multi-channel 3 3 convolution
Input
K of these
Line Buffer
Double Buffer

## Slide 4: Challenges with Jade CGRA
Memory supports only line buffered pipelines
  Most new applications even for imaging and vision use neural networks
  Need a memory hierarchy with double buffers for energy-efficiency
Multi-channel 3 3 convolution
K of these
1. Bring in tiles of inputs and weights into local memory reuse them as much as you can
2. Use a double buffer to overlap compute on current tile and fetching of next tile
3. Use a hierarchy of double buffers to maximize energy-efficiency

## Slide 5: Challenges with Jade CGRA
Configuration over JTAG is slow
  Large applications with multiple kernels don’t fit on the CGRA – need fast reconfiguration

## Slide 6: Key (application driven!) architectural changes in Garnet CGRA
Support for Bfloat16, and for executing complex operations like divide using multiple PEs
Addition of a global buffer to create a memory hierarchy for efficiently executing neural networks, and double buffer support in all memories
Fast reconfiguration support using global buffer and control processor
Addition of configurable power domains

## Slide 7: CGRA
 | Processing Element
 | (PE) / Compute
 | Memory (MEM)
 | Switch box (SB)
 | Connection box (CB)
MEM
MEM
MEM
MEM
PE
PE
PE
PE
PE
PE
PE
PE
MEM
MEM
MEM
MEM
Coarse Grained Reconfigurable Array (CGRA)
Tile

## Slide 8: Interconnect
Keyi Zhang

## Slide 9: Connection Box (CB) - Jade
PE
CB
10 vertical 16 bit tracks
5 driven up, 5 driven down
10 horizontal 16 bit tracks
5 driven left, 5 driven right
10-to-1 mux
A
B
There are similar 1 bit CBs for feeding 1 bit inputs from 10 horizontal and vertical 1 bit tracks
CB
SB

## Slide 10: Connection Box (CB) - Garnet
CB
CB
PE
10 vertical 16 bit tracks
5 driven up, 5 driven down
10 horizontal 16 bit tracks
5 driven left, 5 driven right
2 20-to-1 muxes
B (identical mux as A)
There are similar 1 bit CBs for feeding 1 bit inputs from 10 horizontal and vertical 1 bit tracks
SB
A

## Slide 11: Switch Box (SB)
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
Pipeline register
PE

## Slide 12: Switch Box (SB)
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
0
1
2
3
4
Figure shows connectivity for ‘0’ tracks
Similar connectivity for all other numbered tracks
PE output goes to all muxes
PE

## Slide 13: Processing Element
Nikhil Bhagdikar

## Slide 14: Processing Element (PE) in Diablo
op_a_reg
data0
op_b_reg
Two 16 bit operands
op_d_reg
op_e_reg
Three 1 bit operands
op_f_reg
8 entry
1 bit lut register
res
ALU
Add
Mult
And
…
res_p
clk
clk_en
rst_n
cfg_d
cfg_a
cfg_en
32
8
read_data
irq
32
op_a
data1
op_b
bit0
bit1
bit2
op_d
op_e
op_f
en_acc
flag_sel
Flag Logic
C, V, res_p

## Slide 15: Register Modes
Previous slide shows only this dotted portion
In reality, the register is more complex because of debug functionality
In both modes, the data is registered, in delay mode it is unconditionally registered, in valid mode it is registered only when clk is enabled
reg
data0
cfg_d[15:0]
load = cfg_en && (cfg_a == F0)
rst_n
load or (mode == delay) or ((mode == valid) && clk_en)
mode == bypass
1 0
1 0
0 1
This particular register’s address
Or cfg_d[0] for 1 bit registers

## Slide 16: Accumulation Operation
For b, load signal can also be clk_en & en_acc (bit in the op code that enables accumulation)
The data going into the register can also be 0/output of the PE after accumulation
reg
data0
cfg_d[15:0]
load = (cfg_en && (cfg_a == F1)) |
(clk_en & en_acc)
rst_n
load or (mode == delay) or ((mode == valid) && clk_en)
mode == bypass
1 0
1 0
0 1
en_acc & op_d_p
0 1
0
comp_res
(cfg_en && (cfg_a == F1))
0 1
ALU output
To reset the accumulation register

## Slide 17: Configuration Registers in Diablo
inp_code
rst_n
cfg_en && (cfg_a == FF)
1 0
cfg_d[31:16]
op_code
1 0
cfg_d[15:0]
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
inp_code
mode (a)
mode (b)
en_acc
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
op_code
mode (d)
mode (e)
mode (f)
pe_op_code
flag_sel
irq_en

## Slide 18: Flag Logic
flag_sel
0 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15
res_p
1b
EQ NE CS CC MI PL VS VC HI LS GE LT GT LE LUT ALU
Z ~Z C ~C N ~N V ~V C&~Z ~C|Z N==V N!=V ~Z|(N==V) Z|(N!=V) LUT ALU res_p
C = carry is generated
V = overflow
res 16b
res_p 1b
Z = res == 0
N = res is negative
ALU produces

## Slide 19: Breakpoint in Diablo
debug_data
!=
res
irq_en
debug_bit
!=
res_p
irq_en
irq

## Slide 20: Global Signal Flow
irq (interrupt request) signal is connected to global signal tiles (GST) in a hierarchical tree fashion
PE
PE
PE
PE
irq
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
…

## Slide 21: Reading Diablo registers in debug
debug_data
debug_bit
op_a_reg
op_b_reg
op_d_reg
op_e_reg
Lut
op_f_reg
{inp_code, op_code}
cfg_a
00 E0 E1 F0 F1 F3 F4 F5 FF else
0
read_data
8b
16b
1b
16b
1b
1b
1b
16b
32b
32b

## Slide 22: Clock Gating in Diablo
Each tile has 4 1 bit global signals coming in
These go into all three 1 bit connection boxes
There is another connection box that outputs the cg_en (clock gating enable) signal, reverse of which is the clk_en signal sent to the PE core
  This connection box chooses this cg_en signal from 10 of the routing tracks on side 1 and the 4 global signals
  Block diagram is on next slide

## Slide 23: 1 Bit Connection Boxes in Diablo
4 global signal wires
PE
SB
1 bit tracks
1 bit tracks
CB
D
CB
F
CB
E
CB
cg_en

## Slide 24: Improvements in Lassen over Diablo
Lassen supports 16 bit Bfloat type
  1 b sign, 8 b exponent, 7 bit mantissa
  Same range as Float32
Bfloat add and multiply natively
Micro-instructions to implement Bfloat transcendentals (divide, exp, power, log, sin, cos)
Optimization passes (currently manual) to improve efficiency
Proposed improvements : 16-bit LUT for masking operations
Need review: Are the operations in lassen sufficient for implementing target applications

## Slide 25: Diablo vs Lassen
Diablo Ops
Add
Sub
Abs
GTE_Max
LTE_Min
Sel
Mult0
Mult1
Mult2
SHR
SHL
Or
And
XOr
New Ops in Lassen
FPAdd
FPMult
FGetMant
FAddIExp
FSubExp
FCnvExp2F
FGetFInt
FGetFFrac
Allows easy porting of applications!
Enables new applications that need a large range like DNN training or complex ops like divide
Micro-instructions
Other FP instructions requested by Jeff: sub,
le lt, ge, gt, neq, neq,
neg, flr, ceil, abs, min, max, sqr

## Slide 26: Transcendentals Example - Divide
divident = Data(0x4288) #68
divisor = Data(0x4020) #2.5
quotient = Data(0x41D9) #68/2.5 = 27.2
mant = pe_get_mant(asm.fgetmant(), divisor, Data(0))
lookup_result = mem_lut.div_lut(mant)
scaled_result = pe_scale_res(asm.fsubexp(), lookup_result, divisor)
quotient. = pe_mult(asm.fp_mult(), scaled_result, divident)

## Slide 27: Bfloat LUTs
class tlut:
def div_lut(self, index):
return {
0 : 0x3f80,
1 : 0x3f7e,
2 : 0x3f7c,
…
126 : 0x3f01,
127 : 0x3f00
} [index]
def ln_lut(self, index):

## Slide 28: Memory
Max Strange

## Slide 29: Memory Core in Jade
There is a mux that chooses which one bit control signal goes out
  0, 1, 2, valid, full, almost_full
Two banks both 16 bit wide and 512 entry
There is a read and a write phase

## Slide 30: Memory
Two single port memory banks
FIFO Controller
Line Buffer Controller
Double Buffer Controller
SRAM

## Slide 31: Global Buffer
Taeyoung Kong

## Slide 32: Global Buffer – Main Functions
Highly banked buffer for data reuse
Buffer to store bitstream for parallel reconfiguration
Design Philosophy: Make global buffer simple and flexible

## Slide 33: Global Buffer – Components
Global Buffer
64b
0
1
2
3
28
29
30
31
…
32 SRAM banks
4 MB total
64 bit wide
Bank Array
AXI – bank Interconnect
8 I/O controller + controller<->bank interconnect
I/O controller_0
I/O controller_7
I/O controller_1
I/O controller_6
…
8 config controller + controller<->bank interconnect
Config controller_0
Config controller_7
Config controller_1
Config controller_6
…

## Slide 34: Global Buffer – SoC interface
0 | 1 | 2 |  | 31
CGRA appears as a Memory to the SoC
SoC provides a wrapper that converts between this simple interface into AXI interface which has block transfers
  Block = 256 words * 64 bits/word
Pipelined to support high clock frequency
wdata (64b)
waddr
wen
raddr
ren
rdata (64b)
Address Decoders
To/from SoC

## Slide 35: Global Buffer – I/O controller
0 | 1 | 2 | 3 | 4 | 
16 x 32 CGRA
28 | 29 | 30 | 31
Global Buffer
64b
0
1
2
3
…
4
28
29
30
31
din
addr
addr
dout
Configurable in modes, number of types, capacity for different data
…
…
I/O controller_0
I/O controller_7
Inputs
Weights

## Slide 36: Global Buffer – I/O controller
To CGRA, we send out data and valid
From CGRA, we get data and valid
Start_addr
Addr
Num_word
Addr
Gen
Ren
16b Data
Valid
64b Data
Addr
Addr
Gen
Ren
16b Data
Valid
64b Data
<FIFO mode>
<SRAM mode>
Addr_high
Addr_low
Ren

## Slide 37: Global Buffer – Parallel Reconfiguration
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | … | 28 | 29 | 30 | 31
32 CGRA Columns
32 SRAM Banks
8 config controllers
Configuration Bus
{config_write,
32b config_addr,
32b config_data}
Configuration Bus from Global Controller
Global Address
Decode Logic
Generates rden, addr
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | … | 28 | 29 | 30 | 31
data
…
…

## Slide 39: Global Controller
Taeyoung Kong & Alex Carsello

## Slide 40: Configuration – AXI4-Lite & JTAG
JTAG is able to write/read to CGRA configuration and TOP configuration
AXI4-Lite is able to write to TOP configuration
Global
controller
tck
tdi
trst
tms
tdo
wr_en
wr_addr[15:0]
wr_data[31:0]
rd_addr[15:0]
rd_data[31:0]
rd_en
interrupt
JTAG
AXI4-Lite
wrapper
Global buffer
Parallel Config Controller
CGRA
configuration
bus
TOP configuration bus

## Slide 41: CGRA control – start & done
Block level of application is controlled by cgra_start and cgra_done
Global
controller
Global buffer
I/O controller
cgra_start_pulse
cgra_done_pulse
Input
data
output
data
Input
data

## Slide 42: Global Signal Flow
<River-flowing input>
PE
PE
PE
PE
Global signals
(clk, reset, config_wr)
PE
PE
PE
PE
PE
PE
PE
32’h0
PE
PE
PE
32’h0
config_read_data
<River-flowing output>

## Slide 43: Debug Support by JTAG
JTAG can do everything!
Debug CGRA fabric
  Write/read CGRA-configuration registers
  Write/read SRAM in CGRA fabric
  4bit stall signal
    Every tile has configuration registers to select a stall signal from 4bits
Debug CGRA fabric + global buffer
  Write/read TOP-configuration registers
  Write/read SRAM in global buffer
  Write/read CGRA control register (cgra_start)

## Slide 44: Power Domains
Ankita Nayak

## Slide 45: Motivation
Adoption of ‘Design for PPA’ mindset
Save power by turning off tiles in the fabric not actively used

## Slide 46: Architectural Features
1. Power Switch Network Architecture
2. Boundary protection between
the active and shutdown tiles
3. FT to connect IO near shutdown logic to the active part & for global signals

## Slide 47: ON-OFF Boundary Protection
2. Use the existing muxes in the design
for boundary protection
1. Redesign the muxes in the design to allow for inherent clamping mechanism
AON : Always ON
SD : Shutdown

## Slide 48: Tile Architecture
PS
PS
PS
PS
PS
PS
PS
PS
PS
PS
PS
PS
AON
SD
Configuration register and its decode logic for enabling the power switches is kept ON
Buffers and logic on global signals are kept ON
All other logic is shutdown when the tile is turned OFF
GLOBAL SIGNAL BUFFERS
DECODE LOGIC
PS EN

## Slide 49: Top Level – Different sections can be turned ON/OFF by P&R

## Slide 50: Summary of Garnet architectural features
Support for Bfloat16, and for executing complex operations like divide using multiple PEs
Addition of a global buffer to create a memory hierarchy for efficiently executing neural networks
Fast reconfiguration support using global buffer and control processor
Addition of configurable power domains

## Slide 51: SoC
CGRA
Global Buffer
DMA Engine
DMA Engine
TLX
CoreLink
Control Processor
(ARM Cortex M3)
Nested Vector Interrupt Controller (NVIC)
Wake-up Interrupt Controller (WIC)
Memory Protection Unit (MPU)
I-Bus
D-Bus
Debug JTAG
TLX
DRAM
DRAM Controller
Application Processor
FPGA
SRAM
4 Banks
AXI
AXI
AXI
AXI
AHB
AHB
AHB
SoC