## Slide 1
Next-Generation PE Architecture
Nikhil Bhagdikar
Motivation
Integration
Efficient support for a wider range of applications
Better integration with AHA flow
Improve energy and area efficiency
Data Types
Int4 for machine learning (inferencing)
Int8 for imaging pipelines
Int16 for imaging, vision, and machine learning (training)
B-Floats (16-bit 8+8 floating point)
New Instructions
Non linear functions (log, exponentials, trigonometric)
Packing (eg: two 8-bit objects to a 16-bit word)
Conversion (eg: int to float)
Create a global spec for the PE
Improves compiler/mapper to hardware interface
New instructions are readily absorbed by the flow
Robust verification
Implementing Non Linear Functions
Current Work: Evaluating efficiency tradeoff
  Specialized units
  Specialized routing in existing units
  Non specialized
A new scheme for table based evaluation of functions [David et al., 2006]
Improving Energy/Area Efficiency
PE Area Distribution
*Data from 16nm CGRA chip taped out
Future Work:
  Heterogeneity
  Improved multipliers and pipelining
  Data/Clock gating