## Slide 1: Specifying Multi-PE ops (like cos, 32-bit multiply)
"modules":{
"DesignTop":{
"type":["Record",[
["in",["Record",[["arg_1",["Array",1,["Array",1,["Array",16,"BitIn"]]]]]]],
["out",["Array",1,["Array",1,["Array",16,"Bit"]]]]
]],
"instances":{
"const2__348":{
"genref":"coreir.const",
"genargs":{"width":["Int",16]},
"modargs":{"value":[["BitVector",16],"16'h0002"]}
},
"mul_347_348_349":{
"genref":"coreir.mul",
"genargs":{"width":["Int",16]}
},
"pt_hw_output_2_stencil_p1":{
"genref":"mantle.wire",
"genargs":{"type":["CoreIRType",["Array",1,["Array",1,["Array",16,"Bit"]]]]}
}
},
"connections":[
["mul_347_348_349.in1","const2__348.out"],
["self.in.arg_1.0.0","mul_347_348_349.in0"],
["pt_hw_output_2_stencil_p1.in.0.0","mul_347_348_349.out"],
["self.out","pt_hw_output_2_stencil_p1.out"]
]
}
}
ALL CoreIR primitives should use the Halide JSON format (code to the left) to specify CGRA primitive subgraph, which can be one or multiple ops
Mapper matches the CoreIR primitive to app graph and emits the corresponding CGRA primitive graph to the PnR tool
The CGRA primitive JSON can specify more than just the connectivity for the CGRA primitives eg: it can specify the configuration pattern(s) to enable the primitive(s) that the bitstream writer can use

## Slide 2: Specifying Intra-PE Routing
The mapper needs to pattern match subgraphs from the app to possible subgraphs in the PE. Not all subgraphs in the PE can/should be enumerated.
Need to specify intraPE routing as a graph that the mapper can pattern match to
Need new primitives like “config-mux” that the mapper can manipulate (it cant manipulate the app graph), and can be used as glue to realize complex subgraphs in the PE
Need an operational peak-PE spec from Ross/Raj to comment more. Current way of specifying is good from an enumeration perspective, but perhaps needs more thought for specifying connectivity

## Slide 3: Multiple ops per PE
The IntraPE routing specification should be sufficient to analyze if any two ops can be scheduled parallelly in a PE. This analysis needs to be done by the mapper and the placer for exploiting app and placement locality.
VLIWing is restricted by
  Number of outputs
  Number of hardware resources
  IntraPE routing
An alternative is to enumerate all possible parallel ops and list them as instructions that the compiler/mapper can map to. The enumeration can be automated based on the IntraPE routing spec.

## Slide 4: Packed Arithmetic
App-level packing (eg: RGB channel processing, stereo depth)
  New packed_wire(bit_cnt, tracks) primitive in CoreIR and CGRAPrimitives
  New pack/unpack(bit_cnt_in, tracks_in, bit_cnt_out, tracks_out) primitives in CoreIR and CGRAPrimitives that connect to packed_wire
  New packed_add(bit_cnt, tracks), etc. primitives in CoreIR and CGRAPrimitives that connect to packed_wire
  Packing and OPs can be atomic i.e. in the same PE
PnR-level packing
  Can placer can pack ops?
    What ops can be packed?
    Does placer always use atomic packing/op/unpacking, or can it skip unpacking to create a chain of packed ops? Do we have such opportunities?

## Slide 5: Handling Flags
Certain flags like Z,NZ can be treated as ops themselves and can be applied to intermediate outputs as discussed in the 2nd slide (mapper can map those with pattern matching).
Flags like C,V (and other custom flags) are best defined by the op designer (in a multi output op) [need example peak code]
Need ability to combinatorially munge flags. IntraPE routing specification (along with a LUT) should be sufficient for this
Behavior of all flags at all times is formally known
Next slide covers more of this

## Slide 6: Multibit to single bit and vice versa
Multibit to single bit ops can be specified using existing CoreIR/CGRA primitives (LT,GT).
Single bit to multibit ops (eg: masking, muxing, inverting, counting) need a new CGRA primitives – repeat/extend. CoreIR already has a repeat primitive that can map to the CGRA repeat primitive.
The repeated/extended value can then be used as a multi-bit value.
SB2MB ops can be implemented in the primitives library as two-step ops – repeat/extend followed by the actual OP.
LUT should be extended to perform multibit bitwise operations
Flags can be considered as MB2SB ops

## Slide 7: Floating Point
Conversion to FP
  New CoreIR/CGRA primitive – convertToFp(bits, binary_point_loc, fformat)
  Fixed formats (bfloat, half precision)?
Conversion from FP
  New CoreIR/CGRA primitive – convertFromFp (bits, binary_point_loc, fformat, mode)
  Mode specifies
    how are NaN and inf converted
    how are flags set (if any)
    rounding
Rounding
  New instruction and primitives for rounding are needed
Transcendentals
  New CGRA primitives for pre/post ops
  Multi-PE specification (slide 1) used by the mapper to realize these op for PnR