## Slide 1: Virtual Tapeout Concept
Real tapeout is not very agile
  Requires multiple iterations, usually at the end when design is finished
  First iteration is most painful, successful iterations less so
  Tapeout usually only done ONCE per design cycle!?
Virtual tapeout - still very real!
  But does not (always) go to foundry
  Tapeout early, tapeout often
  Start with simple base chip, iterate as design progresses
  Tapeout / mini-tapeout on every check-in (a la Travis) !!?

## Slide 2: Virtual Tapeout (Tape-In)
Start small: need base flow and a base chip to work from.
  Pad frame only, then pad frame plus one tile, then...
Small/fast per-tool test cases for the flow?
  One for each problem found in the main flow for fast debug
  Each new tool, technology, uses these tests to boot up rapidly
Flow will need info from design to create chip
  Info might include floor planning, power domains, technology details…
  All this extra info needs to be created by the generator
Real chip continually created every (week? commit?)
  To ensure it doesn’t get stale
  Prev-week design is always available when/if crunch time comes

## Slide 3: Proprietary or Open-Source?
Tapeout must run on machines with proprietary library info
  Flow has to seamlessly handle proprietary IP
  How do we do that?
BUT can also use these flows to create a design in an open pdk
This gives a path for the larger design community to help
  Tune the design flow
  Debug the flows to make then technology agnostic